## Slide 1: IoT – Hackathon Room Information Service @ HHZ
Tim Spannagel, Tiemo Bang, Katja Haas, Mehmetcan Korkmaz

## Slide 2: Agenda
Scenario
Value Proposition
Architecture
Hardware
Approach
Live Demo

## Slide 3: Scenario
HHZ 125
Raspberry Pi 3
EnOcean
EnOcean
EnOcean
EnOcean
EnOcean
EnOcean
Dashboard
HHZ 125
Facility Manager
Motion sensor
Light sensor
Temperature sensor
Room Information Service
Actions
Recommendations via

## Slide 4: Value Proposition
Room Information Service @ HHZ for Facility Manager
Emotional: Well done job
Functional: Providing a safe and energy efficient room
Social: Activity by given command avoid personal room checking (extra work)
Extra work (effort)
 physical check of room environment
Unlocked rooms at night
Open windows after classes
  Cold rooms
  Destroyed rooms (e.g. caused by rain, snow)
Minimum effort for manage room environment
Efficient use of energy
Reliability of closed windows and doors
Avoiding of extra work
Motion, light, temperature sensors and sensors at windows provide information about actual status on a dashboard
Dashboard is available at any time (mobile: App)
Sensor information in combination with conditions gives concrete action commands or recommendations
  Example: 22 am, dashboard shows open windows and no motions in room  command to close the windows
EnOcean sensors
Raspberry Pi gateway
Dashboard providing actual status of sensors
Software commanding concrete actions in order to sensor information in combination with specific conditions

## Slide 5: Architecture
Hardware Layer
Software Layer
Controller (Raspberri Pi 3 Model B)
Gateway (USB 300)
Dashboard
Window Sensor
(Wireless magnet contact STM 250 (OEM)
Door Sensor
(Wireless magnet contact STM 250 (OEM)
Event Processing
(NodeJS Socket IO)
E-Mail
Temperatur Sensor
(NodOn-STP - 2-1-03 EnOcean-Sensor)
MQTT Publisher
(HHZ MQTT Broker)
MQTT Subscriber
(HHZ MQTT Broker)
Google calendar

## Slide 6: Live Demo

## Slide 7: Questions?

## Slide 8: Thank you!